; Partslist for New_RFE HA-SDR Filter Unit, Version 0.91

; Date:   2009-10-04

:Author:  Hans Brandl, Munich, Germany; DC4MG;  hans.brandl@gmx.net; www.brandl.de.tc

;-------------------------------------------------------------------------------

Change History:  First published version: V0.9, 2009-09-07

Changes for V0.91:    IC11 added

C214 C216 corrected

; -----------------------------------------------------------------------------------------------------------------------------

Pos	Sheet Qty.	Part Numbers	Value	Type	Vendor Order Number

1	1	64	C1, C2, C4, C10, C11, C13, C14, C16, C17, C18,	0.1 uF	SMD C0805	Reichelt

2		C30, C37

3		C201, C202, C203, C207, C208,			Buerklin

3		C211, C212, C213, C217, C218,

3		C221, C222, C223, C227, C228,

3		C231, C232, C233, C237, C238,

3		C241, C242, C243, C247, C248,

4		C33

5		C251, C252, C253, C257, C258,

5		C261, C262, C263, C267, C268,

5		C271, C272, C273, C277, C278,

5		C281, C282, C283, C287, C288,

5		C291, C292, C293, C297, C298

6		C18

2	1	1		C08	10 nF	SMD C0805

3	1	5		C12, C13, C14, C15, C5	22 nF	SMD C0805

4	2	6	C79, C80, C126, C81, C82, C47	47 nF	SMD C0805

5	1	4	C5, C6, C7	0.22 uF	SMD C0805

4		C101

6	2	2	    C28, C19	1 uF	SMD C0805

7	1	2		C03, C09	4.7 u	Elko radial E2.5-6

8	2	2	C29, C30, 	10 uF	Elko radial E2.5-5

10	1	1	L1	10 uH	Wired 0207/7

11	2	2	L2	100 uH	SMD L4532C

12	1	4	L3, L4, L5, L6, L7	22 uH 	SMD L3230M

13	1	4	L9	22 uH 	SMD L4532P

14	2	2	L21, L22	10 uH	Wired 0207/15

15      4	6	L31, L32, L33, L34, L35, L36	22 uH	SMD L1206

Pos	Sheet Qty.	Part Numbers	Value	Type	Vendor Order Number

20	1	1	R7	3.3 Ohm	R0805

21	1	3	R12, R13, R25	5.1 Ohm	R0805

22	1	2	R26, R27	10 Ohm	R0805

23	1	1	R23	27 Ohm	R0805

24	1	6	R3, R4, R5, R29, R31, R32	51 Ohm	R0805

25	1	2	R18, R19 	56 Ohm	R2010

26	2	5	R1, R2	100 Ohm	R0805

1		R15, R17, R24 	100 Ohm	R0805

27	1	1	R28	220 Ohm	R0805

28	1	1	R6	470 Ohm	R0805

29	6	2	R61, R68	680 Ohm	R0805

30	1	4	R8, R9, R10, R11	1 KOhm	R0805

31	6	2	R62, R69	1 KOhm	R0805

32	1	2	R14, R16	3.3 KOhm	R0805

33	6	1	R64	10 Kohm	R0805

34	6	3	R65, R66, R67	33 Kohm	R0805

;----------------------------------------------------------------------------------------------------------------------------------

40	6	7	D1, D3, D5, D70, D69, D71, D72	1N4148W	SMD SOD123

41	1	4	D9, D10, D11, D12	BA595	SMD SOD323-R

42	6	6	D61, D62, D63, D64, D67, D68	PRLL5818	SMD MiniMELF

Pos	Sheet Qty.	Part Numbers	Value	Type	Vendor Order Number

50	4	2	IC1, IC11	ULN2003AD	SMD SO16

51	2	1	IC2	74HC139AD	SMD SO16

52	2	4	IC3, IC4, IC5, IC6	74HC595AD	SMD SO16

53 	2	2	IC7, IC8	74HC04AD	SMD SO16

54	1	1	IC9	74AC86AD	SMD SO16

55	2	1	IC10	OPA2674	SMD SOIC8

56	3	20	IC20, IC21, IC22, IC23,  IC24, IC25,	HMC226	SMD SOT26A 	see www.hittite.com

3		IC26, IC27, IC28, IC29,

5		IC30, IC31, IC32, IC33, IC34, IC35

5		IC36, IC37, IC38, IC39

57	2	1	IC15	SGA 6286	SMD  	see www.sirenza.com 86 package

;--------------------------------------------------------------------------------------------------------------------------------------

60	4	16	K1, K2, K3, K4, K5, K6, K7, K8, K9, 	G5-V1 5V	Relais 	Bürklin, Reichelt

K10, K11, K12,

1		K13, K14, K16, K20

61	1	4	K24, K25, K21, K22	G5-V1 12V !	Relais

61	1	1	K15	G6K-2P 5V	Relais 	Reichelt

61	1	1	K18	G6K-2P12V !	Relais

;--------------------------------------------------------------------------------------------------------------------------------------

70	6	3	Q1, Q2, Q3	BSS123	SMD SOT23

71	6	2	Q4, Q5	BCX53	SMD SOT89

;--------------------------------------------------------------------------------------------------------------------------------------

80	1	1	T1	ADT1.5-1	MCL CD636	Minicircuit Lab or DIY

81	1	1	T2	TC4-1T	MCL CD636 	Minicircuit Lab or DIY

;------------------------------------------------------------------------------------

90	1	5	X-ANT, X-TRX, X-VTR_3, X-EXT-INP, X-EXT-OUT	SMA or MCX Socket   mount on application requirement !

Lowpassfilter  SDR-1000 Parameters, Sheet  3 and 5

Pos	Sheet Qty.	Part Numbers	Value	Type	Vendor Order Number

100	3	1	C295	3300 pF	SMD C1206

101	3	2	C294, C 296	2200 pF	SMD C1206

102	3	1	C275	1500 pF	SMD C1206

103	3	3	C225,C274, C276	1000 pF	SMD C1206

104	3	1	C255	820pF	SMD C1206

105	3	2	C224, C226, 	680 pF	SMD C1206

106	3	3	C245, C254, C256	560 pF	SMD C1206

107	3	1	C235	470 pF	SMD C1206

108	3	2	C244, C246	390 pF	SMD C1206

109	3	1	C285	330 pF	SMD C1206

110	3	2	C234, C236	270 pF	SMD C1206

111	3	3	C265, C284,  C 286	220 pF	SMD C1206

112	3	2	C264, C266	150 pF	SMD C1206

113	3	1	C215	120 pF	SMD C1206

114	3 	2	C214, C216	68 pF	SMD C1206

120	3	2	L211, L212	0.178 uH	Toroid or L4532

121	5	2	L261, L262	0.25 uH	Toroid or L4532

122	5	2	L281, L282	0.35 uH	Toroid or L4532

123	3	2	L231, L232	0.53 uH	Toroid or L4532

124	3	2	L241, L242	0.75 uH	Toroid or L4532

125	3	2	L221, L222	1.39 uH	Toroid or L4532

126	5	2	L251, L252	1.69 uH	Toroid or L4532

127	5	2	L271, L272	1.85 uH	Toroid or L4532

128	5	2	L291, L292	3.76 uH	Toroid or L4532

Bandpass-Filter,  SDR-1000 Parameters, 3 poles, Sheet 4

Pos	Sheet Qty.	Part Numbers	Value	Type	Vendor Order Number

200	4	4	C102, C104, C112, C114	1000 pF	SMD C1206

201	4	1	C113	680 pF	SMD C1206

202	4	2	C122, C124	470 pF	SMD C1206

203	4	2	C132, C134	270 pF	SMD C1206

204	4	2	C142, C144	220 pF	SMD C1206

205	4	1	C123	180 pF	SMD C1206

206	4	2	C152, C154	100 pF	SMD C1206

207	4	1	C133	82 pF	SMD C1206

208	4	1	C153	56 pF	SMD C1206

209	4	1	C143	47 pF	SMD C1206

210	4	2	L102, L104	open	Toroid or L4532

211	4	1	L103	3.9 uH	Toroid or L4532

212	4	4	L113, L123, L133, L143 	2.7 uH	Toroid or L4532

213	4	4	L112, L114, L122, L124	1.8 uH	Toroid or L4532

214	4	4	L132, L134, L142, L144	1.8 uH	Toroid or L4532

215	4	1	L153	0.27 uH	Toroid or L4532

216	4	2	L152, L154	0.15 uH	Toroid or L4532